## Slide 1: LED Fundamentals
Understand your specifications

## Slide 2: About color

## Slide 3
About color
Color is about wavelengths
  Visible light is a small region of the electromagnetic spectrum
  Wavelengths range from 400nm (violet) to 700nm (red)
Seeing color is about perception
  The eye absorbs the light by several receptors
  The brain translates these ‘measurements’ in color sensation
The eye has 2 types of receptors
  Rods are sensitive to low levels of light and do not pickup color
  Cones provide us the ability to sense color and resolve fine detail
    L: Long wavelenght or called Red (peak sensitivity at 564nm)
    M: Mid wavelength or called Green (peak sensitivity at 534nm)
    S: Short wavelenght or called Blue (peak sensitivity at 420nm)

## Slide 4
About color
A color can be created by mixing 3 primary colors
  Additive mixing of several wavelenghts can give the same perception as a pure color of one single wavelenght
  The exact quantity of Red, Green and Blue (the primaries) needed to create another pure color has been measured by means of an experiment
The result is the CIE 1931 Color Space
Experiment
Mapping of RGB for each color
CIE 1931 color space

## Slide 5
About color
The CIE 1931 color space
  This shows a full plot of all colors that the human eye can see
  The outer curved boundary is the monochromatic locus
  The White Point D65 is white at color temperature of 6500K
A color gamut is a section
  The boundaries are defined by its primary colors
  Several gamuts exist, such as HDTV, NTSC, EBU, LED, ...
    CRT: depending on the colors of the phosphors of the monitor
    HDTV: uses the sRGB color gamut based on CRT
    LED: depending on the colors of the Red, Green and Blue led used
The larger the gamut, the more saturated the colors
  A device that is able to reproduce the entire visible color space is still an unrealized goal
  LED screens have a very large gamut => more saturation
    That’s why LED is sometimes preferred over projection

## Slide 6
About color
The color of each pixel is defined by
  Amount of light emitted by the Red LED (r)
  Amount of light emitted by the Green LED (g)
  Amount of light emitted by the Blue LED (b)
But each LED has some tolerances on
  Wavelength
  (x,y) coordinates
  Luminous Intensity
This means that for another pixel, with the same values of (r), (g) and (b) a different color might be shown
The solution to this problem is
  Reduce tolerances by carefully selecting the LEDs
    This is also called ‘ranking’ or ‘binning’
    The narrower the selection is, the more expensive the LEDs are
  Calibration
G2
G1
R1
R2
B1
B2
Color difference
r
b
g
Calibrated Green
G2
G1
Adding some red
Adding some blue
Bring all LEDs of same color together

## Slide 7
About color
You would be surprised how much Blue and Red is contained in Green

## Slide 8: About specifications

## Slide 9: Basic specifications of a LED product
Understanding the specifications is key !!!
  Comparing with different type of products
  Determining the correct product type for an application
  Giving the correct explication to customers
Specifications can be misleading
  Interpretations might differ from vendor to vendor
  Understanding the specs = know what you talk about
After all... it’s no rocket science

## Slide 10: Configuration – SMD or TH
2 types of LEDs
  Through-Hole (TH)
  Surface Mounted Diode (SMD)
TH
  At least one LED per color (Red, Green, Blue)
  Sometimes a 4th or even 5th LED is added to:
    Increase brightness
    Allow virtual pixel mode
    Create better color reproduction (depends on LED brand)
  Used for larger pitches (>10mm) -> Outdoor applications
SMD
  3 colors in one package
  Allows wider viewing angles (less color shift)
  Allows shorter viewing distances (color mixing happens earlier)
  Used for smaller pitches (<10mm) -> Indoor applications
  “Black silicon resin” or “Black package” to increase contrast
TH
SMD
Configuration |  | 
 | Pixel pitch | mm
 | LED configuration | SMD or TH
 | LED per pixel | 3 or 4
 | LED density | LED/sqm
 | Pixel mode | Real/Virtual
 | Hor pixels | pixels/tile
 | Ver pixels | pixels/tile
 | Pixel density | pixels/sqm

## Slide 11: Configuration – “Black” LED
Configuration |  | 
 | Pixel pitch | mm
 | LED configuration | SMD or TH
 | LED per pixel | 3 or 4
 | LED density | LED/sqm
 | Pixel mode | Real/Virtual
 | Hor pixels | pixels/tile
 | Ver pixels | pixels/tile
 | Pixel density | pixels/sqm
Barco to be the first to use “Black LED” (BK)

## Slide 12: Configuration – Pixel density
“Pixel” <> “LED”
  LED refers to the physical component that creates a pixel
  Pixel is the smallest component of the image
    In case of TH: pixel = multiple LEDs
    In case of SMD: pixel = LED
Different layouts of TH pixels
  3 LEDs (R, G, B) -> most common
  4 LEDs (R, R, G, B) –> example V10v
  Other formats might be possible
Different layouts of SMD pixels
  RGB in line
  RGB in ‘mickey mouse’ pattern
Density
  LED-density = LEDs/sqm
  Pixel-density = Pixels/sqm
    In case of TH, LED-density > pixel-density
TH RRGB
TH RGB
SMD
Configuration |  | 
 | Pixel pitch | mm
 | LED configuration | SMD or TH
 | LED per pixel | 3 or 4
 | LED density | LED/sqm
 | Pixel mode | Real/Virtual
 | Hor pixels | pixels/tile
 | Ver pixels | pixels/tile
 | Pixel density | pixels/sqm

## Slide 13: Configuration – Pixel pitch
The “pixel pitch” is the distance between pixels
  Center to Center
  Normally: vertical = horizontal
Resolution of LED-screen
  “Horizontal pixels per tile” x horizontal tiles
  “Vertical pixels per tile” x vertical tiles
Virtual pixel mode
  Combining LEDs of adjacent pixels to create additional pixels
  Increases the resolution of LED screen...
    without adding LEDs
    without increasing power consumption
  Usage
    Excellent for moving images
    Not recommended for still images (<sharpness)
  Example V10v -> 20 mm real / 10mm virtual
Configuration |  | 
 | Pixel pitch | mm
 | LED configuration | SMD or TH
 | LED per pixel | 3 or 4
 | LED density | LED/sqm
 | Pixel mode | Real/Virtual
 | Hor pixels | pixels/tile
 | Ver pixels | pixels/tile
 | Pixel density | pixels/sqm

## Slide 14: Configuration – Pixel pitch
Pixel pitch determines minimum viewing distance
  Minimum viewing distance ‘= pitch in meter’
    Relates to color mixing – all leds in a pixel merge in to a single colored pixel
    Is shorter for SMD than TH
  Optimal Viewing Distance ‘= pitch in meter x 2’
    Where viewer can not see any pixelization
    Is shorter for TH than SMD
Screen size determines maximum viewing distance
  Maximum Viewing Distance ‘= vertical size x 30’
    Is rather subjective – related to screen size and readablility
    Readability means that the type of content is important (still or moving images, text)
Configuration |  | 
 | Pixel pitch | mm
 | LED configuration | SMD or TH
 | LED per pixel | 3 or 4
 | LED density | LED/sqm
 | Pixel mode | Real/Virtual
 | Hor pixels | pixels/tile
 | Ver pixels | pixels/tile
 | Pixel density | pixels/sqm
Rules of thumb!!!

## Slide 15: Configuration – Pixel pitch
Size of screen when displaying text
  Depends on number of lines to be displayed
  Be careful with virtual pixels – use real pixels to calculate
Configuration |  | 
 | Pixel pitch | mm
 | LED configuration | SMD or TH
 | LED per pixel | 3 or 4
 | LED density | LED/sqm
 | Pixel mode | Real/Virtual
 | Hor pixels | pixels/tile
 | Ver pixels | pixels/tile
 | Pixel density | pixels/sqm

## Slide 16: Configuration – Pixel pitch – case study
Configuration |  | 
 | Pixel pitch | mm
 | LED configuration | SMD or TH
 | LED per pixel | 3 or 4
 | LED density | LED/sqm
 | Pixel mode | Real/Virtual
 | Hor pixels | pixels/tile
 | Ver pixels | pixels/tile
 | Pixel density | pixels/sqm
Displays with text require accurate ‘pitch-study’
  Scoreboards
  Information displays

## Slide 17: Performance - Brightness
Performance |  | 
 | Brightness (calibrated @ 6500K) | NIT
 | Contrast Ratio | w:b
 | Color processing/Gray scale | bit/color
 | Colors | #
 | Dimming | bit
 | Horizontal Viewing Angle (color shift) | deg
 | Horizontal Viewing Angle (50% brightness) | deg
 | Vertical Viewing Angle (color shift) | deg
 | Vertical Viewing Angle (50% brightness) | deg
 | Max Power Consumption | W/sqm
 | Typ Power Consumption | W/sqm
 | Operating Power Voltage and frequency | V Hz
 | Typical LED Lifetime | hrs
Brightness of LED-tile is expressed in NIT
  Each LED generates a light output in candela
  A pixel generates the combined light output of its (R, G, B) LEDs
  Brightness is expressed in NIT: 1 NIT = 1 candela per sqm
  Pixel density x cd/pixel = brightness in NIT
Each LED tile is factory calibrated
  To eliminate the differences in brightness between seperate LEDs
  To guarantee same color for each pixel (%R, %G, %B)
  Barco uses “Narrow binning” LEDs -> highest quality
Color temperature is important parameter
  Calibration is done at a color temperature of 6500K
  The color temperature gives a normalized combination of R, G , B
Screen brightness is calibrated on site
  The installation software alligns to the ‘weakest tile’
  Without site calibration, tiles might be perceived brighter/darker

## Slide 18: Performance – Contrast ratio
Performance |  | 
 | Brightness (calibrated @ 6500K) | NIT
 | Contrast Ratio | w:b
 | Color processing/Gray scale | bit/color
 | Colors | #
 | Dimming | bit
 | Horizontal Viewing Angle (color shift) | deg
 | Horizontal Viewing Angle (50% brightness) | deg
 | Vertical Viewing Angle (color shift) | deg
 | Vertical Viewing Angle (50% brightness) | deg
 | Max Power Consumption | W/sqm
 | Typ Power Consumption | W/sqm
 | Operating Power Voltage and frequency | V Hz
 | Typical LED Lifetime | hrs
Contrast ratio is ratio between white and black
  White is created by emitting light
  Black is created by blackness of tile surface
Black is more difficult to create then white
  Depends on blackness of LEDs used
  Depends on blackness of material between LEDs used
  Depends on reflective behavior of material used
  Depends on external light conditions
    Contrast ratio to be measured at surounding light of 200 Lux
Barco’s louvre design acts as ‘light trap’
  Reflected light is trapped to create darker surface
  For elevated screens, short louvres improve viewing, but reduce contrast ratio
Better blackness reduces power consumption
  Less emitted light needed for same contrast

## Slide 19: Performance – Processing
Performance |  | 
 | Brightness (calibrated @ 6500K) | NIT
 | Contrast Ratio | w:b
 | Color processing/Gray scale | bit/color
 | Colors | #
 | Dimming | bit
 | Horizontal Viewing Angle (color shift) | deg
 | Horizontal Viewing Angle (50% brightness) | deg
 | Vertical Viewing Angle (color shift) | deg
 | Vertical Viewing Angle (50% brightness) | deg
 | Max Power Consumption | W/sqm
 | Typ Power Consumption | W/sqm
 | Operating Power Voltage and frequency | V Hz
 | Typical LED Lifetime | hrs
Typical LED tile building blocks
  Windowing/Grabber to take a part of the image
  Gamma correction to adjust unlinearities between input and output
  Digital Contrast to control the overall brightness
  Calibration to guarantee color uniformity
  LED driving PWM (Pulse Width Modulation) to drive the brightness of each individual LED

## Slide 20: Performance – Processing
Performance |  | 
 | Brightness (calibrated @ 6500K) | NIT
 | Contrast Ratio | w:b
 | Color processing/Gray scale | bit/color
 | Colors | #
 | Dimming | bit
 | Horizontal Viewing Angle (color shift) | deg
 | Horizontal Viewing Angle (50% brightness) | deg
 | Vertical Viewing Angle (color shift) | deg
 | Vertical Viewing Angle (50% brightness) | deg
 | Max Power Consumption | W/sqm
 | Typ Power Consumption | W/sqm
 | Operating Power Voltage and frequency | V Hz
 | Typical LED Lifetime | hrs
“16 bits per color”
  Each color (LED) has an accuracy of 16 bits
  16 bits = 216 = 65536 different combinations
    0 = no light = black
    65536 = full brightness (R, G or B)
  R x G x B = 281000000000000 or 281 trillion combinations
But why 16 bits if video input is < 16 bits?
  Example: Blue Ray player only offers 8 bits/color
Higher internal bits/color results in better color reproduction
  Especially for “low lights”  “flat” side of gamma curve
Inaccurate
color reproduction
Accurate
color reproduction

## Slide 21: Performance – Processing
Performance |  | 
 | Brightness (calibrated @ 6500K) | NIT
 | Contrast Ratio | w:b
 | Color processing/Gray scale | bit/color
 | Colors | #
 | Dimming | bit
 | Horizontal Viewing Angle (color shift) | deg
 | Horizontal Viewing Angle (50% brightness) | deg
 | Vertical Viewing Angle (color shift) | deg
 | Vertical Viewing Angle (50% brightness) | deg
 | Max Power Consumption | W/sqm
 | Typ Power Consumption | W/sqm
 | Operating Power Voltage and frequency | V Hz
 | Typical LED Lifetime | hrs
Dimming
  There are 2 ways to dim (reduce brightness)
    Only use the “darker” R, G and B
      This also reduces the combinations for each color
      Color steps will become visible at low brightness
    Use a seperate dimming control
      Even at low brightness, all combinations for each color are possible
  Barco uses a seperate dimming control of 8 bits
    8 bits = 28 = 256 steps = 0,4% per step
    Human eye doesn’t see differences less than 2%

## Slide 22: Performance – Viewing angle 1
Performance |  | 
 | Brightness (calibrated @ 6500K) | NIT
 | Contrast Ratio | w:b
 | Color processing/Gray scale | bit/color
 | Colors | #
 | Dimming | bit
 | Horizontal Viewing Angle (color shift) | deg
 | Horizontal Viewing Angle (50% brightness) | deg
 | Vertical Viewing Angle (color shift) | deg
 | Vertical Viewing Angle (50% brightness) | deg
 | Max Power Consumption | W/sqm
 | Typ Power Consumption | W/sqm
 | Operating Power Voltage and frequency | V Hz
 | Typical LED Lifetime | hrs
Viewing angle (color shift)
  Angle at which the color of the screen changes
    Because of LEDs being covered by other LEDs
    Because louvres obstructing some LEDs
  Left and Right will always be equal (120° = +60°/-60°)
  Up (+) will in most cases be smaller than down (-)
Color shifts to green

## Slide 23: Performance – Viewing angle 2
Performance |  | 
 | Brightness (calibrated @ 6500K) | NIT
 | Contrast Ratio | w:b
 | Color processing/Gray scale | bit/color
 | Colors | #
 | Dimming | bit
 | Horizontal Viewing Angle (color shift) | deg
 | Horizontal Viewing Angle (50% brightness) | deg
 | Vertical Viewing Angle (color shift) | deg
 | Vertical Viewing Angle (50% brightness) | deg
 | Max Power Consumption | W/sqm
 | Typ Power Consumption | W/sqm
 | Operating Power Voltage and frequency | V Hz
 | Typical LED Lifetime | hrs
Viewing angle (50% brightness)
  Angle at which the output of the LED is reduced to 50%
  It does not mean that brightness of SCREEN is reduced to 50%
    At an angle, more LEDs/sqm are seen
    Brightness = cd/LED (reduced) x LED/sqm (increased)
    In the below example, brightness still 70% at angle of 50% brightness

## Slide 24: Performance – Power consumption
Performance |  | 
 | Brightness (calibrated @ 6500K) | NIT
 | Contrast Ratio | w:b
 | Color processing/Gray scale | bit/color
 | Colors | #
 | Dimming | bit
 | Horizontal Viewing Angle (color shift) | deg
 | Horizontal Viewing Angle (50% brightness) | deg
 | Vertical Viewing Angle (color shift) | deg
 | Vertical Viewing Angle (50% brightness) | deg
 | Max Power Consumption | W/sqm
 | Typ Power Consumption | W/sqm
 | Operating Power Voltage and frequency | V Hz
 | Typical LED Lifetime | hrs
Power consumption of LED tile is combination of
  Power for controller, ventilators, etc... -> ‘Black power’
  Power for LEDs -> R, G, B power
  Even when not emitting light, the tile consumes power
Usage of the power consumption specifications
  Maximum power consumption
    Used to calculate power provisions
    Used to calculate LED-tiles/power-circuit
  Typical power consumption
    Used to calculate power provisions
    Used to calculate LED-tiles/power-circuit
Typical power consumption is only an estimate
  Depends on image content (white consumes more than black)
  Depends on brightness of screen
    Using automatic brightness control might significantly reduce power consumption
  Barco LiveDots is known as ‘green product’
Example: TF-20

## Slide 25: Performance – Typical LED Lifetime
Performance |  | 
 | Brightness (calibrated @ 6500K) | NIT
 | Contrast Ratio | w:b
 | Color processing/Gray scale | bit/color
 | Colors | #
 | Dimming | bit
 | Horizontal Viewing Angle (color shift) | deg
 | Horizontal Viewing Angle (50% brightness) | deg
 | Vertical Viewing Angle (color shift) | deg
 | Vertical Viewing Angle (50% brightness) | deg
 | Max Power Consumption | W/sqm
 | Typ Power Consumption | W/sqm
 | Operating Power Voltage and frequency | V Hz
 | Typical LED Lifetime | hrs
Light output of LEDs gradually decreases
Lifetime specification
  Light output drops below 50%
  Used at typical brightness (+/- 30% of maximum)
Barco commonly specifies 100000 hrs
  That is 11,4 years when used 24/7
  In most cases this far exceeds warranty expectations

## Slide 26: Some applications

## Slide 27: LED-screen – Basic

## Slide 28: LED-screen – DOOH
Combination of a LED Image Processor and an X2O player results in very compact design
All content loaded (buffered) on HardDisk of X2O player
Direct connection to IP-network (through customer network)
Remote Management System allows management of several screens
AEC allows 24/7 operation in light-sensitive environments (roads, city centers, ...)

## Slide 29: LED-screen – Multiple large screens

## Slide 30: LED-screen – DOOH – Connection to network
Network connection can not be provided by Barco
Examples (see left images)
  Telenet home network
  ClearChannel/Cemusa 3G
Fiber also possible
  although less common for multiple DOOH screens

## Slide 31: Signal transmission: Fiber using patch cables

## Slide 32: Image processing: Multiple screens with 1 input/1 output
This approach can be cost saver for
  Double sided screens
  Cubes
Distance between screens is limited to maximum cable lenght
  DVI: appx. 4 meter
  NNI: appx. 10 meter
  VVI: appx. 60 meter
  InifinipixTM: appx. 60 meter
Only one AEC can be used
  not AEC for V-series
  InifinipixTM allows more than one AEC controlled via NM100
LED Image Processor maps images on correct tiles
Can be extended over fiber in most cases

## Slide 33: Image processing: Combining multiple inputs to one screen
For almost half of the price
  More inputs to your screen
  More control of your inputs
  Smoother transitions between inputs

## Slide 34: Image processing: Practical example -> Scoreboard
PiP allows overlay
Video effects available
Multiple inputs available

## Slide 35
Questions & Answers
Thanks for your Attention